## Slide 1: VASM Architecture 2020
Brief Introduction of VASM Architecture
By Tigran Khachatryan

## Slide 2: Վիրտուալություն
Virtual Machine Ln (Software)
…
Virtual Machine L1 (Software)
Actual Machine L0 (Hardware)

## Slide 3: Կոմպիլյացիա և Ինտերպրետացիա
Interpretation
Compilation
Source Code:
Translation
Compilation
Linking
Executable Program
Execution
Command Interpretation
Next Command
Binary Code:

## Slide 4: Համակարգչի կառուցվածքը Computer Organization
Computer
Processor (CPU)
I/O Devices
Memory
(RAM)
I/O Devices
System BUS
I/O Devices
North Bridge
South Bridge

## Slide 5: Մեքենայական Հիշողության Մոդելը Computer Memory
Միավոր (Byte = 8 Bit)
Հասցեավորում = 32 Bit
Գծային Հասցեական տարածություն 0-232-1
Մեքենայական բառ Byte = 1 bytes Word = 2 bytes DWord = 4 bytes QWord = 8 bytes
Default = DWord
0x00000000
0x00000004
0x00000008
0xFFFFFFF8
0xFFFFFFF4
0xFFFFFFFC
…
0
31
QW
B
W
DW
Address
Data
1,2,4 or 8 bytes
…

## Slide 6: Registers
Address Registers
Status Register
FLAGS : 32
IP : 32
SP (R8) : 32
SF (R12) : 32
RIP (R4) : 32
A0 (R16) : 32
A1 (R20) : 32
A2 (R24) : 32
A3 (R28) : 32
General Purpose Registers
R32 : 8
R33 : 8
…
R63 : 8
Hidden Registers
IR : 64
IP = Instruction Pointer
RIP = Return IP
SP = Stack Pointer
SF = Stack Frame
IR = Instruction Register
Read-Only Zero Register
R0 : 32 = 0

## Slide 7: Register Pool
R0-R3 Ռեգիստորները ծրագրին հասանելի են միայն կարդալու համար և մշտապես հավասար են 0-ի (սակայն պրոցեսորն այն օգտագործում է որպես IP)
R4-R15 Ռեգիստորները հասանելի են գրելու կարդալու և գործողություններ կտարելու համար սակայն ունեն առանձնահատուկ նշանակություն
R16-R31 ռեգիստորները նույնպես հասանելի են բայց նաև կարող են օգտագործվել որպես հասցեավորման ռեգիստորներ A0-A3
R32-R63 ընդհանուր նշանակության ռեգիստորներ են և հասանելի են թվաբանական և տրամաբանական գործողություններ կատարելու համար
QW
B
W
DW
0
0
0
0
0
31
RIP
SP
SF
A0
A1
A2
A3
R3 – R0
R7 – R4
R11 – R8
…
R63 – R60
R15 – R12
R19 – R16
R23 – R20
R27 – R24
R31 – R28
R35 – R32

## Slide 8: Register and Memory Alignment
Ռեգիստորների և Հիշողության յուրաքանչյուր բայթ հասանելի է, սակայն 4-ի բաժանվող ինդեքսով բայթը (byte) կարելի է գրել-կարդալ միայն 4-ի բաժանվող հասցեով և հակառակը։ Համապատասխանաբար 4-ի բաժանելուց 1,2 և 3 մնացորդով ինդեքսները կարելի է գրել-կարդալ միևնույն մնացորդով հասցեով և հակառակը։
Նույնկերպ 4-ի բաժանելուց 0 և 2 մնացորդով հասանելի բառը (word) կարելի է գրել-կարդալ միևնույն մնացորդով ինդեքսով կամ հասցեով։ Բառը կենտ մնացորդով ինդեքսով կամ հասցեով գրել-կարդալ հնարավոր չէ և արգելված է։
Կրկնակի բառը (DWord) հնարավոր է գրել- կարդալ միայն անմնացորդ 4-ի բաժանվող ինդեքսներով և հասցեներով։
Քառակի բառը (QWord) կարելի է գրել-կարդալ միայն անմնացորդ 8-ի բաժանվող ինդեքսներով և հասցեներով։
B
W
DW
R4+1
R4
R4+2
R4+3
Alignment
RAM (Little Endian)
4xAddress
Byte
Byte
Byte
Byte
Word
Word
Double Word

## Slide 9: FLAGS
CF: Carry Flag
ZF: Zero Flag
SF: Sign Flag
OF: Overflow Flag
Carry Flag. Set if an arithmetic operation generates a carry or a borrow out of the most-significant bit of the result; cleared otherwise. This flag indicates an overflow condition for unsigned-integer arithmetic. It is also used in multiple-precision arithmetic.
Zero flag. Set if the result is zero; cleared otherwise.
Sign flag. Set equal to the most-significant bit of the result, which is the sign bit of a signed integer. (0 indicates a positive value and 1 indicates a negative value.)
Overflow flag. Set if the integer result is too large a positive number or too small a negative number (excluding the sign-bit) to fit in the destination operand; cleared otherwise. This flag indicates an overflow condition for signed-integer (two’s complement) arithmetic.
z
…
0
n-1
s
n
z
CF
x
…
x
x
y
…
y
y
Arithmetic/Logic Operation
OF
s
SF
1:0
ZF
Result == 0 ?
1:0
?
?
1:0
Operand1:
Operand2:
CF
ZF
SF
Reserved (0)
0
1
2
3
15
OF
Not Availabe
32

## Slide 10: Memory Access Operations
Load [B,W,DW,QW] Dest. ← [Address]
Destination Reg. = RAM[Address]
Store [B,W,DW,QW] [Address] ← Source
RAM[Address] = Source Reg.
Load Relative Dest. ← [Base ± Offset]
Dest. Reg. = RAM[Base Address ± Offset]
Store Relative [Base ± Offset] ← Source
RAM[Base Address ± Offset] = Source Reg.
Rn+1
Rn
QW
B
W
DW
Rn+2
Rn+3
Rn+4
Rn+5
Rn+6
Rn+7
RAM (Little Endian)
Operand Size Bytes
Address

## Slide 11: Move Operations
MOVI Dest. ← Number (8, 16 or 32 Bit)
Destination Reg. = Number
Move [B,W,DW,QW] Dest. ← Source
Destination Reg. = Source Reg.
Swap [B,W,DW,QW] Dest. ← Source
Temp = Dest. Reg.
Dest. Reg. = Source Reg.
Source Reg. = Dest. Reg.
Move Immediate Value
Rn+1
Rn
B
W
DW
Rn+2
Rn+3
Command
Num8
Num16
Num32
Rt+1
Rt
Rt+2
Rt+3
Rt+4
Rt+5
Rt+6
Rt+7
QW
B
W
DW
Rs+1
Rs
Rs+2
Rs+3
Rs+4
Rs+5
Rs+6
Rs+7
Move/Swap Values Between Registers

## Slide 12: Bitwise Logical Operations
AND, OR, XOR
Opr. [B,W,DW,QW] Dest. ← Source
Dest. Reg. = Dest. Reg. opr. Source Reg.
Flags: SF=Sign bit, ZF=(Res.== 0), CF = OF = 0
NOT [B,W,DW,QW] Dest.
Dest. Reg. = ~(Dest. Reg)
Flags: SF=Sign bit, ZF=(Res.== 0), CF = OF = 0
z
…
0
n-1
s
n
z
CF
x
…
x
x
y
…
y
y
Logic Operation
OF
s
SF
1:0
ZF
Result == 0 ?
0
0
Destination
Operand:
Source
Operand:
Destination
Operand:
=
!x
…
0
n-1
!s
n
!x
CF
x
…
s
x
OF
s
SF
1:0
ZF
Result == 0 ?
0
0
Destination
Operand:
Destination
Operand:
=
NAND, NOR
Opr. [B,W,DW,QW] Dest. ← Source
Dest. Reg. = Not(Dest. opr. Source)
Flags: SF=Sign bit, ZF=(Res.== 0), CF = OF = 0

## Slide 13: Shift Operations
x
x
x
…
0
1
2
3
n-1
x
b
n
x
b
CF
0
Shift Logical Left:
b
x
x
…
0
1
2
3
n-1
x
x
n
x
0
CF
b
Shift Logical Right:
x
x
x
…
0
1
2
3
n-1
x
b
n
x
b
CF
0
Shift Arithmetic Left:
Shift Arithmetic Right:
b
x
x
…
0
1
2
3
n-1
x
s
n
x
CF
b
s
SHL, SHR, SAL, SAR
Shift [B,W,DW,QW] Destination ← Count
Dest. Reg. = Dest. << >> Count (Reg. or Num)
CF=Last shifted out bit, ZF=(Res.==0), SF=MSB,
OF = SHL|SAL(MSB==CF ? 0:1),
SAR(0), SHR(MSB)

## Slide 14: Rotate Operations
Rotate Logical Left:
Rotate Logical Right:
Rotate with Carry Left:
Rotate with Carry Right:
x
x
x
…
0
1
2
3
n-1
x
b
n
x
b
CF
b
b
x
x
…
0
1
2
3
n-1
x
x
n
x
CF
b
b
x
x
x
…
0
1
2
3
n-1
x
b
n
x
b
CF
cf
b
x
x
…
0
1
2
3
n-1
x
x
n
x
CF
b
cf
ROL, ROR, RCL, RCR
Rotate [B,W,DW,QW] Destination ← Count
Dest. Reg. = Dest. rotate Count (Reg. or Num)
CF=Last shifted out bit, ZF=unchanged, SF=unchanged,
OF = <<(CF xor MSB)
>> (MSB1 xor MSB2)

## Slide 15: Negative numbers Two’s complement
Representation of
Signed numbers:
Sign Bit: 0 – Positive, 1 – negative number
x
…
s
x
x
0
1
n-1
n
Representation of 1:
0
…
0
0
1
Representation of -1:
1
…
1
1
1
Representation of MAX:
1
…
0
1
1
Representation of -MAX:
0
…
1
0
1
Representation of MIN:
0
…
1
0
0
Representation of 0:
0
…
0
0
0
Sign Conversion
-Num = NOT(Num) + 1
=
y
…
!s
y
y
0
1
n-1
n
x
…
s
x
x
!x
…
!s
!x
!x
Not(Num)
-N:
N:
+1

## Slide 16: Type Conversion
Cast Up:
b
b
b
…
0
1
2
15
16
s
x
31
x
Before Sign Extension
…
x
30
b
b
b
…
0
1
2
15
16
s
s
31
s
…
After Sign Extension
s
30
Cast Down:
After Truncation
b
b
b
…
0
1
2
15
16
b
b
31
b
Before Truncation
…
b
30
b
b
b
…
0
1
2
15
16
s
0
31
0
…
0
30

## Slide 17: Arithmetical Operations Unsigned & Signed Addition, Subtraction, Negation
ADD, SUB, ADC, SBB
Opr. [B,W,DW,QW] Dest. ← Source
Dest. Reg. = Dest. Reg. ± Source Reg. (± CF)
Flags: SF=Sign, ZF=(Res.== 0), CF = Transfer from MSB ? 1:0, OF = Transfer from MSB2 to MSB1 ? 1:0
NEG [B,W,DW,QW] Dest.
Dest. Reg. = -(Dest. Reg)
Flags: SF=Sign, ZF=(Res.== 0), CF=(Src.==0) ? 0:1, OF = Transfer from MSB2 to MSB1 ? 1:0
z
…
0
n-1
s
n
z
CF
x
…
x
x
y
…
y
y
OF
s
SF
1:0
ZF
Result == 0 ?
1:0
1:0
Destination
Operand:
Source
Operand:
Destination
Operand:
=
MSB: Most Significant Bit
LSB: Least Significant Bit
Transfer from MSB2 to NSB1
Carry
Overflow
Transfer from MSB
…
0
n-1
MSB1
n
MSB2
LSB
z
…
0
n-1
s
n
z
CF
!x
…
!s
!x
OF
s
SF
1:0
ZF
Result == 0 ?
0:1
1:0
Destination
Operand:
Destination
Operand:
=
+1

## Slide 18: Arithmetical Operations Unsigned & Signed Multiplication
MUL, IMUL
Opr. [B,W,DW,QW] Dest. ← Source
2x Dest. Reg. = Dest. Reg. * Source Reg.
Flags: SF=ZF=undefined,
CF=OF=(Transfer from LowerHalf to UpperHalf) ? 1:0
Signed Multiply
If (Dest. < 0) Dest. = -(Dest.)
If (Src. < 0) Src. = -(Src.)
2x Dest. = Dest. * Src.
If (Dest. < 0 xor Src. < 0)
2xDest. = -(2xDest.)
z
…
0
n-1
z
n
z
x
…
x
x
y
…
y
y
CF/OF
1:0
Destination
Operand:
Source
Operand:
2x Destination
Operand:
z
…
n+1
2n
z
2n+1
z
?
Product

## Slide 19: Arithmetical Operations Unsigned & Signed Division
DIV, IDIV
Opr. [B,W,DW,QW] 2x Dest. ← Source
Lower Half Dest. Reg. = 2x Dest. / Src.
Upper Half Dest. Reg. = 2x Dest. MOD Src.
Flags: SF=ZF=CF=OF=undefined,
Signed Divide
If (2xDest. < 0) Dest.= -(2xDest.)
If (Src. < 0) Src. = -(Src.)
LH Dest. = 2x Dest. / Src.
UH Dest. = 2x Dest. % Src.
If (2xDest. < 0 xor Src. < 0)
LH Dest. = -(LH Dest.)
y
…
y
y
Source
Operand:
2x Destination
Operand:
x
…
0
n-1
x
n
x
x
…
n+1
2n
x
2n+1
x
Dividend
Divizor
2x Destination
Operand:
z
…
0
n-1
z
n
z
r
…
n+1
2n
r
2n+1
r
Reminder
Quotient
Upper Half
Lower Half

## Slide 20: Test & Comparison
TEST [B,W,DW,QW] Dest. ← Source
Temp Res. = Dest. Reg. AND Source Reg.
Flags: SF=Sign bit, ZF=(Res.== 0), CF = OF = 0
CMP [B,W,DW,QW] Dest. ← Source
Temp Res. = Dest. Reg. - Source Reg.
Flags: SF=Sign, ZF=(Res.== 0), CF = Transfer from MSB ? 1:0, OF = Transfer from MSB2 to MSB1 ? 1:0
Void
Operand1
=
&
Operand2
Void
Operand1
=
Operand2
MVI A0, a
LOD R32, A0
TEST R32, R32
JZ Endif
…
Endif:
…
If (a != 0)
{
…
}
MVI A0, a
LOD R32, A0
MVI A1, b
LOD R36, A1
CMP R32, R36
JBE Endif
…
Endif:
…
If (a > b)
{
…
}

## Slide 21: Execution Transfer JUMP
JUMP Absolute
IP = Address (A0-A3)
JUMP CC Offset
IF (CC)
IP += ±Offset (IMM or Rn)
JUMP Relative
IP += ±Offset (IMM or Rn)
0x00000000
Address
IP
Code
JUMP
0xFFFFFFFF

## Slide 22: Execution Transfer Function Call
0x00000000
Address
IP
Code
RET
0xFFFFFFFF
CALL Absolute
RIP = IP
IP = Address (A0-A3)
RETURN
IP = RIP
CALL

## Slide 23: Stack
SP (Top)
1,2,4,8, … bytes
Data
PUSH
SP = SP – N (1,2,4,8)
RAM[SP] = R (1,2,4,8 bytes)
POP
R = RAM[SP] (1,2,4,8 bytes)
SP = SP + N (1,2,4,8)
0x00000000
0xFFFFFFFF
Stack
Stack

## Slide 24: Stack Frame
PUSH SF [Rn|Offset16]
SP = SP – 4
RAM[SP] = RIP
SP = SP – 4
RAM[SP] = SF
SF = SP
(SP = SP – Rn|Offset16)
POP SF
SP = SF
SF = RAM[SP]
SP = SP + 4
RIP = RAM[SP]
SP = SP + 4
(SP = SP + Rn|Offset16)
0xFFFFFFFF
SP (Top)
Stack
Arguments
…
…
Ret Val Addr
Stack
Return IP
SF (Base)
0x00000000
Previous SF
Local Variables
Return Value
Calle Stack Frame
Caller Stack Frame
-
+

## Slide 25: Input Output
IN Rn ← Port [N] (1,2,4,8,… byte)
IN Rn ← Port [Rn] (1,2,4,8,… byte)
OUT Port [N] ← Rn (1,2,4,8,… byte)
OUT Port [Rn] ← Rn (1,2,4,8,… byte)
0x00
0x01
0x02
0xFF
…
Console Device
Future
Devices
I/O Port Address Space
0x04
0x05
0x03
IO Controller
0x06
0x07

## Slide 26: Instruction Format
2 Byte:
4 Byte:
0
OpCode
Reserved
OpCode
Rn
8
OpCode
Extension
Rn
Reserved
OpCode
Extension
Rn1
Rn2
OpCode
Rn
Immediate16
OpCode
Extension
Immediate16
0
8
OpCode
Extension
Rn
Imm8
16
24
OpCode
Rn
0
8
16
24
Immediate32
32
40
6 Byte:
8 Byte:
OpCode
Rn1
0
8
16
24
Immediate32
32
40
Extension
Rn2
48

## Slide 27: Ծրագրի Կառուցվածքը
.data
Static Data
.code
Code
Stack
Dynamic
Data
0x00000000
0xFFFFFFFF
Global Var1
Global Var2
Function 1
Function 2
Function 3
It is OS Loaders responsibility to load the Program from the Executable binary file into the RAM, arrange segments and finalize the Linkage.

## Slide 28: Program Execution
Fetch Instruction
Decode Current Instruction
Next Instruction
Execute Current Instruction

## Slide 29: Program Execution
Fetch: IR = [IP]
Decode:
Switch (OpCode)
IP += CmdLen
Execute

## Slide 30: Starting Computer
Fetch: IR = [IP]
Decode:
Switch (OpCode)
IP += CmdLen
Execute
Initialization:
IP = 0
FLAGS = 0
R0…R63 = 0
…

## Slide 31: Մուտքային Ասեմբլեր լեզվի սահմանումը
Ասեմբլեր լեզուն բաղկացած է 4 մասից՝
  Ստեկի հատվածից (.stack), որտեղ սահմանվում է ծրագրային ստեկի համար անհրաժեշտ ծավալը
  Տվյալների հատվածից (.data), որտեղ սահմանվում են ընդհանուր փոփոխականները և սկզբնարժեվորվում
  Կոդի հատվածից (.code), որտեղ սահմանվում են ֆունկցիաները
  Գլխավոր ֆունկցիայի սահմանման հատվածից (.main), որտեղ նշվում է ծրագրի մուտքային ֆունկցիայի անունը
Փոփոխականները սահմանվում են նշելով տիպը, անունը և ըստ անհրաժեշտության արժեքը։
Հրամանը կարող է ունենալ օգտագործվելիք տվյալի չափսը նշող նախդիր (B=byte, W=word, DW=double word, QW=quad word), օր․՝ MOV W R0,R2: Տվյալի լռելյայն (default) չափսը DW-ն է։
Փոփոխականների և Ֆունկցիաների անվանումները ծառայում են որպես համապատասխան հասցեի փոխարինողներ։

## Slide 32: Մուտքային Ասեմբլեր լեզվի օրինակ
# Assembly file sample
.STACK = 1024
# Variables section
.DATA
BYTE var # Variable definition without initialization
CHAR ch1 = ‘A’ # Variable definition with initialization statement
CHAR str1[] = "Hello World!“ # Variable array (String)
BYTE bVal1; # Forward declaration
BYTE bVal2 = 255
BYTE abVal3[] = 0x4F,0x0F # Array size will be determined by its initializer list
BYTE abVal4[10] # Array size explicitly specified but not initialized
WORD wVal5 = -10
DWORD dwVal6 = 0xA0B0C0D0
DWORD adwVal7[5] = 10,20,30,-40,0x0F00
QWORD qwVal9 = 0xFFFFFFFFFFFFFFFF
# Functions
.CODE
Func PrintString; # Function forward declaration
Func Start: # Function definition
ASSIGN A0, str1
ASSIGN A1, PrintString
CALL A1
RET
EndF # End of function body
Func PrintString
PUSHSF
…
JUMP Label1:
…
Label1: POPSF
RET
EndF
.MAIN = Start # Entry point definition

## Slide 33: Instruction Set
Control
NOP // No operation
BREAK // Debug break point
END // End of program
JUMP/JMP An // Jump absolute
JUMP/JMP Rn| ±Offset16 // Jump relative (unconditional)
J(cc) Rn| ±Offset16 // Jump relative if condition is true
CALL An // Call a subroutine by absolute address
RET // Return from the subroutine to the caller

## Slide 34: Instruction Set
Condition Codes
xE / xZ (zf=1) // do x if Equal / Zero (==)
xNE / xNZ (zf=0) // do x if Not equal / Not zero (!=)
xA / xNBE (cf=0 & zf=0) // do x if Above / Not below and equal (>)
xAE / xNB (cf=0) // do x if Above or equal / Not below (>=)
xB / xNAE (cf=1) // do x if Below / Not above or equal (<),
xBE / xNA (cf=1 | zf=1) // do x if Below or equal / Not above (<=)
xG / xNLE (zf=0 & sf=of) // do x if Great / Not low or equal (signed)
xGE / xNL (sf=of) // do x if Great or equal / Not low (signed)
xL / xNGE (sf<>of) // do x if Low / Not great or equal (signed)
xLE / xNG (zf=1 | sf<>of) // do x if Low or equal / Not great (signed)
xO (of=1) // do x if Overflow (sign changed)
xNO (of=0) // do x if Not overflow (sign changed)
xS (sf=1) // do x if Negative (signed)
xNS (sf=0) // do x if Not negative (signed)

## Slide 35: Instruction Set
Memory access
LOAD/LOD An, [An] // Load into Address register from memory (DW)
LOAD/LOD [oprsz] Rn, [An] // Load GP register from memory (B,W,DW,QW)
STORE/STO [An], An // Store from Address register into memory (DW)
STORE/STO [oprsz] [An], Rn // Store from GP reg. into memory (B,W,DW,QW)
LDREL An, [An, ±Offset32] // Load relative
LDREL [oprsz] Rn, [An, ±Offset32] // Load relative
STREL [An, ±Offset32], Rn // Store relative
STREL [oprsz] [An, ±Offset32], Rn // Store relative

## Slide 36: Instruction Set
Stack
PUSHSF [Rn|Offset16] // make stack frame
POPSF [Rn|Offset16] // clear stack frame
PUSH An // push address register
POP An // pop address register
PUSH [oprsz] Rn, [Count] // push GP registers
POP [oprsz] Rn, [Count] // pop GP registers

## Slide 37: Instruction Set
Move Immediate value (Assignment)
MOVI/MVI An, Address32 // Assign Double word to address register
MOVI/MVI Rn, Numer8 // Assign Byte to GP register
MOVI/MVI Rn, Numer16 // Assign Word to GP register
MOVI/MVI Rn, Numer32 // Assign Double word to GP register
Assignment of Quad word to GP register does not exist but could be done with two sequential DWord assignment instructions
Move Between Registers
MOVE/MOV [cc] An|Rn, An|Rn // Move between Addr. & GP registers
MOVE/MOV [cc] [oprsz] Rn, Rn // Move bytes between GP registers
SWAP/SWP [cc] An|Rn, An|Rn // Swap Address & GP registers
SWAP/SWP [cc] [oprsz] Rn, Rn // Swap bytes between GP registers

## Slide 38: Instruction Set
Flags
MOVF/MVF Rn // Move (get) Flags into R
SETF/STF Rn // Move (set) Flags from R
CLC // Clear Carry flag (CF=0)
STC // Set Carry flag (CF=1)
CMC // Complement Carry flag (CF=!CF)
ST(cc) [oprsz] Rn // Set register to 1 if CC, 0 otherwise
Comparison
TEST An|Rn, An|Rn // FLAGS = Op1 & Op2
TEST [oprsz] Rn, Rn // FLAGS = Op1 & Op2
CMP An|Rn, An|Rn // FLAGS = Op1 – Op2
CMP [oprsz] Rn, Rn // FLAGS = Op1 – Op2

## Slide 39: Instruction Set
Logical (bitwise)
AND [oprsz] Rn, Rn // Op1 = Op1 & Op2
OR [oprsz] Rn, Rn // Op1 = Op1 | Op2
XOR [oprsz] Rn, Rn // Op1 = Op1 ^ Op2
NAND [oprsz] Rn, Rn // Op1 = ~(Op1 & Op2)
NOR [oprsz] Rn, Rn // Op1 = ~(Op1 | Op2)
NOT [oprsz] Rn // Op1 = ~Op1
All above instructions also are updating FLAGS accordingly

## Slide 40: Instruction Set
Rotate
ROL [oprsz] Rn ← Rn|Count // Rotate target logical left N bits
ROR [oprsz] Rn ← Rn|Count // Rotate target logical right N bits
RCL [oprsz] Rn ← Rn|Count // Rotate target with carry left N bits
RCR [oprsz] Rn ← Rn|Count // Rotate target with carry right N bits
Shift
SHL [oprsz] Rn ← Rn|Count // Shift target logical left N bits
SHR [oprsz] Rn ← Rn|Count // Shift target logical right N bits
SAL [oprsz] Rn ← Rn|Count // Shift target arithmetic left N bits
SAR [oprsz] Rn ← Rn|Count // Shift target arithmetic right N bits

## Slide 41: Instruction Set
Integral Arithmetic
ADD [cc] [oprsz] Rn ← Rn // Op1 = Op1 + Op2
ADC [cc] [oprsz] Rn ← Rn // Add with carry, Op1=Op1+Op2+CF
SUB [cc] [oprsz] Rn ← Rn // Op1 = Op1 - Op2
SBB [cc] [oprsz] Rn ← Rn // Sub with borrow, Op1=Op1-Op2-CF
NEG [cc] [oprsz] Rn // Two’s complement negation (Op=-Op)
All above instructions also are updating FLAGS accordingly
MUL [oprsz] Rn ← Rn // 2xOp1 = Op1 * Op2
IMUL [oprsz] Rn ← Rn // Signed multiply
DIV [oprsz] Rn ← Rn // 2xOp1 = Op1 / Op2, Op1 mod Op2
IDIV [oprsz] Rn ← Rn // Signed divide
Above instruction aren’t affecting flags

## Slide 42: Instruction Set
Address manipulation
INC [cc] An ← Rn // Increment address by Rn
INC An ← Offset16 // Increment address by Immediate value
DEC [cc] An ← Rn // Decrement address by Rn
DEC An ← Offset16 // Decrement address by immediate value
Input & Output
IN [oprsz] Rn ← Rn|Port // Read from I/O Port into target operand
OUT [oprsz] Rn|Port ← Rn // Write 2nd Operand to I/O Port
Type Conversion
CAST oprsz_src oprsz_trgt Rn // Sign extension

## Slide 43: Instruction Set
FPU Registers & Instructions … (TBD)
SSE Registers & Instruction … (TBD)
String Instructions … (TBD)
Cache control Instructions … (TBD)
Atomic Instructions … (TBD)
Branch Prediction Instructions … (TBD)
System Instructions (protected mode) … (TBD)
Debug Registers & Instructions … (TBD)
Other Instructions …

## Slide 44: Debugging Break Instruction
Code Before
Instruction 1
Instruction 2
…
Instruction N
Instruction 3
Instruction 4
Debugger
Instruction 3
Address
Code After
Instruction 1
Instruction 2
…
Instruction N
BREAK
Instruction 4
At breakpoint saves the command and replaces with BREAK

## Slide 45: Debugging Break Instruction
Debugger
Instruction 3
Address
Code
Instruction 1
Instruction 2
…
Instruction N
BREAK
Instruction 4
When execution reaches to the BREAK instruction control passes to debugger
Then it processes the breakpoint and waits for the User commands
INT 3

## Slide 46: Debugging Break Instruction (Break)
Debugger
Instruction 3
Address
Code
Instruction 1
Instruction 2
…
Instruction N
Instruction 3
Instruction 4
Debugger restores the instruction and passes control back to the Program
IRET

## Slide 47: Կարգավորիչի հրահանգները
Help | ? Supported commands listing
Info Prints information about current state and program being debugged
Run [-dbg yes|no] Runs program from current IP (either in debug or nondebug mode)
Trace [Num=1] Step In, executes Num instructions
Next [Num=1] Step Over, executes Num instructions by overcoming function calls
Stepo Step Out, executes program until current function will return
Pause Pauses curent exécution
Reset Resets CPU to initial state
BP [src:line_num|label|func_name] Sets debug break point at specified position
RBp [src:line_num|label|func_name] [all] Removes specified breakpoint
Set [IP src:line|label|func_name] Sets specified value to the specified register
[A(idx) src:line|label|func_name|var_name|0xAddress]
[R(idx) [B|W|DW|QW|CH] +/-num|0xValue]
[CF|ZF|SF|OF 0|1]
Assign [var_name +/-num|0xValue[,...] Assigns value to the specified variable or memory location
BT Prints current backtrace, see also 'print callstack
Dump -f|file file_path Dumps entire memory content or part of it to a file
-format text|bin"<< std::endl;
code [-at src:line|label|func_name] [-size byte_count] Dumps only code started from beginning or at specified address
data Dumps data content only
stack [-depth Num=MAX] Dumps the content of the stack with specified call depth
Print [state] Prints CPU current state
callstack Prints function call stack (same as backtrace)
ports Prints I/O Devices and Port ranges occupied by them
code [-sz|size instruction_count] Prints code started from the current IP or specified address
[-at srs:line|label|func_name|0xAddress]
bp Prints Break points list
sf Prints current stack frame
Watch [var_name [...]] Prints current value of the specified variables
add var_name Ads specified variable to the watch list
rem var_name Removes specified variable from the watch list"<< std::endl;
Load exec_file_path Opens specified binary exectuavle file and loads into memory
Open source_file_name[,...] Opens specifeid source file(s), compiles & loads them into memory
Exit Exits the program and quits